## Slide 1: Fieldbus
Pneumatic Subsystem
Robot Controller
ATI Toolchanger
Laser scan subsystem
Load Cell Subsystem
High speed network switch
Computer

## Slide 2: Notes
Most of the subsystems have either ether cat or ethernet built in, so I used that communication system as the base. Since the pneumatic systems don’t seem to have an ethernet port we would need to add ADCs and DACs with ethernet connection to send over and receive the low-level information.
Since the Pneumatic system is meant to hold the sheets of metal while the arm forms it into the correct shape, it only needs to be activated before and after the robotic system moves. I would move it onto a different system.
Every other system helps the robotic arm move and read either how much pressure the arm is imposing(load cell) or reading how much it has deformed the sheet(laser scanner) or to switch the different size ends for the different requirements in the formation of the sheet(ATI toolchanger)

## Slide 3: Power system
Pneumatic Subsystem
Robot Controller
ATI Toolchanger
Laser scan subsystem
Load Cell Subsystem
Power Rail + Overcurrent protection
120VAC

## Slide 4
Pneumatic Subsystem
Digital Controller
DIN 11mm connector
NITRA Pneumatic Solenoid Valve
AVS+AC0-5322+AC0-24D
ADC to ethernet reader
M12 connector
Low-High
Differential
Wire
Digital control wire
Both controllers are to be determined
VEVOR Electric Hydraulic Pump
Ethernet
Ethernet
24VDC
120 VAC

## Slide 5
Sunrise Instruments Load Cell
M4347D
Sunrise Instruments Control Box
M8128
EEG 2K.316.CCC
24 Volts
DB9 Connector
Ethernet
Load Cell Subsystem

## Slide 6
Keyence laser scanner
LJ-V7000
Controller LJ-V700
Head cable
Ethernet
Laser scan subsystem
24 Volts
FK-MC 0.5

## Slide 7
ATI Toolchanger
QC+AC0-150
ATI Sensor Interface Plate System
SIP
MD12 Connector
Up to 600 Volts
Ethernet
ATI Toolchanger
DK8 master and DK4 tool ethernet modules
MD12 Connector

## Slide 8
Robot Controller
KR C2 controller
Ethernet
Control cables